## Slide 1
Multimodal Diffusion Policy
Teaching a robot arm to move expressively using diffusion models
1 Demo Data
2 DDPM Train
3 CFG Trick
4 U-Net
5 DDIM
6 VLM Judge
7 Metrics
train_cfg.py (slides 2-4) eval_cfg_vlm.py (slides 5-7)
Franka Panda . PyBullet . Two-Block Pick Task

## Slide 2
DDPM Training — The Robot Learns by Denoising
Add noise to demonstrations, train the network to undo it
2 / 7
The Idea (3 steps)
1. Take a clean action chunk a0
2. Add random noise up to T=100 levels
3. Train the network: given noisy aₜ + level t, predict the noise
Noise Schedule (α̅ₜ = how much signal remains at step t)
β₁…βₜ linearly 0.0001 → 0.1 α̅ₜ = β₁ x β₂ x ... x βₜ
Forward Process (add all noise in ONE shot)
aₜ = √α̅ₜ · a₀ + √(1 − α̅ₜ) · ε ε ~ N(0, I)
Training Loss (mean squared error on the predicted noise)
L = E [ || ε - εθ(aₜ, t, obs) ||^2 ] εθ = network prediction, obs = robot observation
EMA Shadow Weights (saved; used at eval time)
θ_ema <- 0.999 x θ_ema + 0.001 x θ
Training Loop (one batch)
1
Pick random noise level t
t ~ Uniform(0, 100) each batch
2
Corrupt the action a0 -> at
One-shot formula above
3
Network predicts noise e_hat
e_hat = e_theta(at, t, obs)
4
Loss = MSE(e_hat, e)
Backprop + AdamW update
5
Update EMA weights
Slow-moving copy of the model
The network solves just ONE random denoising step per batch - not the full 100-step chain.

## Slide 3
Classifier-Free Guidance (CFG)
One model, four behaviors - no separate models needed
3 / 7
The Problem
We want the robot to behave differently (legibly, safely...) using ONE trained model. Behavior is encoded in obs dims 22-25.
The Training Trick (CFG dropout, p=0.15)
Randomly hide the behavior signal during training
obs_tilde = obs with prob 0.85 (behavior-aware) obs_tilde = obs_uncond with prob 0.15 (behavior-blind)
At Inference (steer toward a behavior)
Blend the two predictions with guidance scale lambda
e_hat = e(obs_uncond) + lambda x ( e(obs_cond) - e(obs_uncond) ) lambda=0: no steering lambda=2-4: strong behavior
lambda values:
lambda = 0 ignore behavior, use generic actions
lambda = 1 standard conditional
lambda = 2-4 strongly steered behavior
Behavior Conditioning Dims
Dims 0-21
Base robot state — always present
Dims 22-24
Context XYZ (obstacle or waypoint position)
Dim 25
Behavior mode number
Legibility
mode=1, no context
Safety
mode=3, context = obstacle XYZ
Grounding
mode=4, context = waypoint XYZ
Cost: just 15% random dropout on 4 dims per batch. No extra parameters. No second model.

## Slide 4
U-Net Architecture — The Denoiser Network
Encoder compresses, decoder recovers, skip connections preserve detail
4 / 7
Inputs
Noisy action at
(B, 32 steps, 5 dims)
Observation obs
(B, 26 dims)
Timestep t
(B,) how noisy?
Output: noise prediction
(B, 32, 5) same as at
Time Embedding (encodes noise level t as a vector)
e_t = [sin(t/freq_k), cos(t/freq_k)] then MLP -> 256 dims
Input Fusion (merge action and observation)
x = Linear(at) + MLP(obs) both -> 256 dims
Each Block (linear + norm + activation + skip)
h = Mish( Norm(Linear(x)) + time_proj(e_t) ) out = Mish( Norm(Linear(h)) + shortcut(x) )
Network Flow
Input x = Linear(at) + MLP(obs)
256 ch
Encoder Block 1 + time
256->512
Encoder Block 2 + time -> save skip
512->1024
Bottleneck (global context)
1024->1024
Decoder Block 1 + skip from Enc2
2048->512
Decoder Block 2 + skip from Enc1
1024->256
Output Linear -> predicted noise
256->5
Skip connections: encoder detail goes directly to the decoder -> sharp noise predictions.

## Slide 5
DDIM Sampling — Fast Action Generation at Test Time
20 steps instead of 100 | eta=0.5 for diversity | K=4 candidates
5 / 7
Why DDIM?
DDPM trained 100 steps but we only NEED 20 steps at inference. DDIM skips levels with negligible quality loss -> 5x faster.
Step 1 — Estimate clean action from current noisy version
a0_hat = ( at - sqrt(1 - alpha_t) * e_hat ) / sqrt(alpha_t)
Step 2 — Move to the previous (less noisy) level
a_{t-1} = sqrt(alpha_{t-1}) * a0_hat + sqrt(1 - alpha_{t-1} - sigma^2) * e_hat + sigma * z sigma = eta * sqrt(...) z ~ N(0,I) eta=0.5
CFG applied at EVERY step (steers toward behavior)
e_hat = e_uncond + lambda * ( e_cond - e_uncond )
Denormalize final output back to real joint space
a_real = a0_hat * std_actions + mean_actions
Why K = 4 Candidates?
eta=0.5 adds different random noise each run -> 4 different trajectories from the same observation.
Candidate 1: start pure noise -> 20 DDIM steps -> action chunk (32 steps)
Candidate 2: start pure noise -> 20 DDIM steps -> action chunk (32 steps)
Candidate 3: start pure noise -> 20 DDIM steps -> action chunk (32 steps)
Candidate 4: start pure noise -> 20 DDIM steps -> action chunk (32 steps)
All 4 sent to VLM scorer -> pick the highest-scoring one
eta=0: same trajectory every time (no diversity). eta=0.5: balanced variety for VLM selection.

## Slide 6
VLM Judging — Gemini 3 Pro Picks the Best Trajectory
6 frames per candidate -> behavior question -> score 0 to 1
6 / 7
Pipeline (per episode)
1
Reset sim + place scene objects
Obstacle or waypoint per behavior type
2
Generate K=4 candidates
CFG-DDIM, eta=0.5
3
Capture 6 frames each candidate
t=0s 1s 2s 3s 4s 5s (JPEG 240x240)
4
Ask Gemini 3 Pro
Frames + behavior question in one call
5
Parse score from JSON response
score: 0.91, cue: "early left lean"
6
Run best + worst candidates
Record video, measure path metrics
What Gemini Is Asked Per Behavior
Legibility
How EARLY can you tell which block the arm is going for? 0 = cannot tell at all 1 = obvious from frame 1
Predictability
How STRAIGHT and DIRECT is the path? 0 = curved or erratic 1 = perfectly straight
Safety
How much SPACE does the arm keep from the obstacle? 0 = nearly hits it 1 = wide arc around it
Grounding
Does the arm PASS NEAR the waypoint before picking? 0 = ignores waypoint 1 = clearly visits it
No Gemini fine-tuning. No reward function. VLM judges behavior from video like a human observer.

## Slide 7
Evaluation Metrics — Four Geometric Numbers
Computed on the actual executed trajectory after VLM selection
7 / 7
L_early (Legibility)
L_early = avg P(correct goal | position) over first 30% of path
Uses distance to each goal block as Bayesian signal
-> Higher = arm reveals goal earlier
Path Efficiency (Predictability)
path_eff = straight-line dist / actual path length
1.0 = perfectly straight, below 1 = curved or backtracking
-> Higher = more direct
Clearance (Safety)
clearance = minimum distance to obstacle over all steps
Obstacle radius = 3.5 cm. Clearance > 5 cm = safe
-> Higher = safer
Hover Dist (Grounding)
hover_dist = minimum XY distance to waypoint over all steps
Did the arm pass near the instructed landmark?
-> Lower = better
Compare VLM-steered (best of K) vs baseline (worst of K) -- same model, same checkpoint, only selection differs.

## Slide 8
Summary
Component
What It Does
Key Formula
DDPM Training
L = E[ || e - e_theta(at, t, obs) ||^2 ]
DDPM Training
CFG Dropout
e_hat = e_uncond + lambda * (e_cond - e_uncond)
CFG Dropout
U-Net
x = Linear(at) + MLP(obs), 256->512->1024->512->256->5
U-Net
DDIM Sampling
a0_hat = (at - sqrt(1-alpha_t)*e_hat) / sqrt(alpha_t)
DDIM Sampling
VLM Judging
score in [0,1] per behavior -> select best
VLM Judging
Metrics
VLM-steered vs baseline (same model)
Metrics
One model . One training run . Behavior selected at inference via lambda and obs conditioning . VLM judges without fine-tuning