## Slide 1
Week 1: Environment Design & Demonstration Collection
TwoBlockPick for Legible Robot Motion
Anudeep Gottapu | Arizona State University | Spring 2026

## Slide 2
Problem Motivation
In shared workspaces, robots must communicate intent through motion
A human watching a robot reach for one of two objects needs to predict the goal early
Ambiguous trajectories → human waits → slower collaboration
Legible trajectories → early prediction → efficient teamwork
Research Question: Can we train a generative policy to produce task-successful AND legible trajectories?

## Slide 3
TwoBlockPick Environment
Parameter | Value
Robot | Franka Panda 7-DOF
Physics | PyBullet, dt=1/240s
Objects | Two red blocks, 4cm each
Left block | (0.50, +0.07, 0.42)
Right block | (0.50, -0.07, 0.42)
Jitter | ±0.015m per block
Success | Lift block above z=0.52m
Obs (22-dim): ee_pos + ee_quat + grip + block poses | Act (5-dim): Δx, Δy, Δz, Δyaw, grip

## Slide 4
Camera Setup (Critical for VLM)
Camera: yaw=135°, pitch=-30°, distance=0.9m, FOV=60°
Image-LEFT = World-RIGHT (and vice versa)
Goal A = image-left = world-right block
Goal B = image-right = world-left block
This mapping was initially incorrect and caused evaluation errors.
Getting this right was essential for VLM scoring accuracy.

## Slide 5
Demonstration Collection Strategy
400 Expert Demos via Analytical Bézier Curves
Style | Count | Design
Legible (50%) | 200 | Quadratic Bézier, control point toward goal. Commitment by t≈0.3
Neutral (25%) | 100 | Quadratic Bézier, control point at y=0. No lateral signal
Deceptive (25%) | 100 | Cubic Bézier, P1 feints wrong side, P2 commits correct
10 block configurations × 40 demos each
20 pick-left + 20 pick-right per configuration
Each demo: full episode (up to 400 steps) of obs-action pairs

## Slide 6
Data Format: demos_combined.npz
Array | Shape | Type
obs | (400, 400, 22) | float32
actions | (400, 400, 5) | float32
labels | (400,) | 'left' or 'right'
style_labels | (400,) | 0=legible, 1=neutral, 2=deceptive
config_id | (400,) | 0-9

## Slide 7
Why Three Trajectory Styles?
Legible demos are the target behavior we want the policy to produce
Neutral demos represent baseline “shortest path” behavior
Deceptive demos are worst case — feinting before committing
Mixed training data lets us evaluate whether the policy learns meaningful style differences
Enables VLM evaluation: does the VLM correctly rank styles by legibility?

## Slide 8
Key Design Decisions
Simulation over real robot — Enables 400 demos + reproducible evaluation
Analytical trajectories — Bézier curves give precise control over shape
Symmetric block placement — Legibility comes purely from trajectory shape
3 trajectory styles — Ground truth for evaluating VLM discrimination